## Slide 1: Hands-on
Francisco Muñoz-Martinez
francisco.munoz2@um.es
Universidad de Murcia (UM)

## Slide 2: Agenda
Time (PT) | Topic | Presenter
1:40 – 2:00 | Flexible Accelerators | José L. Abellán
2:00 – 2:20 | Cycle accurate simulation and Overview of STONNE | José L. Abellán
2:20 – 3:20 | (Hands-on) STONNE | Francisco Muñoz-Martínez
3:20 – 3:40 | Coffee Break | 
3:40 – 4:10 | (Hands-on) SST-STONNE | Francisco Muñoz-Martínez
4:10 – 4:40 | (Hands-on) OMEGA | Raveesh Garg
4:40 – 5:00 | Roadmap and Concluding Remarks | Tushar Krishna
https://stonne-simulator.github.io/ASPLOSTUT.html

## Slide 3: Organizers
Tushar Krishna
Associate Professor, School of ECE
Georgia Institute of Technology
tushar@ece.gatech.edu
José L. Abellán
Ramón y Cajal Researcher
University of Murcia
jlabellan@um.es
Manuel E. Acacio
Full Professor
University of Murcia
meacacio@um.es
Raveesh Garg
Ph.D Student
Georgia Institute of Technology
raveesh.g@gatech.edu
Francisco Munoz-Martinez
Postdoc Researcher
University of Murcia
francisco.munoz2@um.es
STONNE Tutorial @ASPLOS 2023
Adrián Fenollar Navarro
Master Student
University of Murcia
adrian.fenollarn@um.es

## Slide 4: Outline
Docker Image, Installation and overview of STONNE.
Hands-on #1: Simulating a real DNN on Flexible DNN Accelerators.
Hands-on #2: Simulating a DNN Layer on Flexagon using SST-STONNE.
Research use cases.
Conclusions.
STONNE Tutorial @ASPLOS 2023

## Slide 5: Outline
Docker Image, Installation and overview of STONNE.
Hands-on #1: Simulating a real DNN on Flexible DNN Accelerators.
Hands-on #2: Simulating a DNN Layer on Flexagon using SST-STONNE.
Research use cases.
Conclusions.
STONNE Tutorial @ASPLOS 2023

## Slide 6: STONNE Repository
STONNE available under the MIT license on Github:
  https://github.com/stonne-simulator/stonne
STONNE Tutorial @ASPLOS 2023

## Slide 7: STONNE Requirements
STONNE dependencies:
  Python 3.6 >= version< 3.9
  C++ 14 or later.
  Anaconda version 2021.05 or older.
  .Linux OS (Tested on Ubuntu 18.05 and Manjaro 21.2.1).
  Not tested in MAC OS.
STONNE Tutorial @ASPLOS 2023

## Slide 8: STONNE Installation
STONNE can be easily installed following a few steps:
  STONNE User interface
STONNE Tutorial @ASPLOS 2023

## Slide 9: STONNE Installation
STONNE can be easily installed following a few steps:
  Pytorch-Frontend
STONNE Tutorial @ASPLOS 2023

## Slide 10: STONNE Installation
STONNE can be easily installed following a few steps:
  Pytorch-stonne
STONNE Tutorial @ASPLOS 2023

## Slide 11: Docker image
To avoid having to install the software, we have set up a docker image which can be directly downloaded and used:
sudo docker run -it stonnesimulator/stonne-simulators
git clone https://github.com/stonne-simulator/tutorials (inside docker)
STONNE Tutorial @ASPLOS 2023

## Slide 12: Docker image
Project organization:
  /STONNE:
    stonne:
      pytorch-frontend
        stonne_connection
      stonne:
        stonne.elf
        Include
        src
        external
        stonne_linker_src
STONNE Tutorial @ASPLOS 2023

## Slide 13: Docker image
Project organization:
  /OMEGA:
    omega
STONNE Tutorial @ASPLOS 2023

## Slide 14: Docker image
Project organization:
  /STONNE
    stonne:
      ASPLOS22
      pytorch-frontend
        stonne_connection
      stonne:
        stonne.elf
        Include
        src
        external
        stonne_linker_src
STONNE Tutorial @ASPLOS 2023

## Slide 15: Docker image
Project organization:
  /STONNE
    stonne:
      pytorch-frontend
        stonne_connection
      stonne:
        stonne.elf
        Include
        src
        external
        stonne_linker_src
STONNE Tutorial @ASPLOS 2023

## Slide 16: Docker image
Project organization:
  /STONNE:
    stonne:
      pytorch-frontend
        stonne_connection
      stonne:
        stonne.elf
        Include
        src
        external
        stonne_linker_src
STONNE Tutorial @ASPLOS 2023

## Slide 17: Docker image
Project organization:
  /STONNE:
    omega
    stonne:
      pytorch-frontend
        stonne_connection
      stonne:
        stonne.elf
        Include
        src
        external
        stonne_linker_src
STONNE Tutorial @ASPLOS 2023

## Slide 18: Docker image
Project organization:
  /STONNE:
    stonne:
      pytorch-frontend
        stonne_connection
      stonne:
        stonne.elf
        Include
        src
        external
        stonne_linker_src
STONNE Tutorial @ASPLOS 2023

## Slide 19: STONNE Source files
/STONNE/stonne/include: Contains the headers
  AccumulationBuffer.h
  Accumulator.h
  ReductionNetwork.h
  ASNetwork.h
  ASwitch.h
  CollectionBus.h
  CollectionBusLine.h
  DistributionNetwork.h
  DSNetworkTop.h
  DSNetwork.h
  DSwitch.h
  MultiplierNetwork.h
  MSNetwork.h
  MultiplierOS.h
  MSwitch.h
  MemoryController.h
  SDMemory.h
  SparseSDMemory.h
  OSMeshSDMemory.h
  Connection.h
  DataPackage.h
  Fifo.h
  STONNEModel.h
STONNE Tutorial @ASPLOS 2023

## Slide 20: STONNE Source files
STONNE organization is able to abstract the main components of the architecture
STONNE Tutorial @ASPLOS 2023

## Slide 21: STONNE Source files
Abstract classes allow to abtract the 4 main components.
  AccumulationBuffer.h
  Accumulator.h
  ReductionNetwork.h
  ASNetwork.h
  ASwitch.h
  CollectionBus.h
  CollectionBusLine.h
  DistributionNetwork.h
  DSNetworkTop.h
  DSNetwork.h
  DSwitch.h
  MultiplierNetwork.h
  MSNetwork.h
  MultiplierOS.h
  MSwitch.h
  MemoryController.h
  SDMemory.h
  SparseSDMemory.h
  OSMeshSDMemory.h
  Connection.h
  DataPackage.h
  Fifo.h
  STONNEModel.h
STONNE Tutorial @ASPLOS 2023

## Slide 22: STONNE Source files
The real hardware comonents implement the abstract classes.
  AccumulationBuffer.h
  Accumulator.h
  ReductionNetwork.h
  ASNetwork.h
  ASwitch.h
  CollectionBus.h
  CollectionBusLine.h
  DistributionNetwork.h
  DSNetworkTop.h
  DSNetwork.h
  DSwitch.h
  MultiplierNetwork.h
  MSNetwork.h
  MultiplierOS.h
  MSwitch.h
  MemoryController.h
  SDMemory.h
  SparseSDMemory.h
  OSMeshSDMemory.h
  Connection.h
  DataPackage.h
  Fifo.h
  STONNEModel.h
Reduction Networks
Distribution Networks
Multiplier Networks
Memory Controllers
Other Useful components
STONNE Tutorial @ASPLOS 2023

## Slide 23: STONNE Source files
Every component implements its void cycle() method which defines the behaviour of the component.
STONNE Tutorial @ASPLOS 2023

## Slide 24: STONNE Source files
/STONNE/stonne/src: Contains the main code
  AccumulationBuffer.cpp
  Accumulator.cpp
  ASNetwork.cpp
  ASwitch.cpp
  CollectionBus.cpp
  CollectionBusLine.cpp
  DSNetworkTop.cpp
  DSNetwork.cpp
  DSwitch.cpp
  MSNetwork.cpp
  MultiplierOS.cpp
  MSwitch.cpp
  MemoryController.cpp
  SDMemory.cpp
  SparseSDMemory.cpp
  OSMeshSDMemory.cpp
  Connection.cpp
  DataPackage.cpp
  Fifo.cpp
  STONNEModel.cpp
STONNE Tutorial @ASPLOS 2023

## Slide 25: STONNE Source files
STONNEModel.cpp drives the simulation based on the user configuration file
  AccumulationBuffer.cpp
  Accumulator.cpp
  ASNetwork.cpp
  ASwitch.cpp
  CollectionBus.cpp
  CollectionBusLine.cpp
  DSNetworkTop.cpp
  DSNetwork.cpp
  DSwitch.cpp
  MSNetwork.cpp
  MultiplierOS.cpp
  MSwitch.cpp
  MemoryController.cpp
  SDMemory.cpp
  SparseSDMemory.cpp
  OSMeshSDMemory.cpp
  Connection.cpp
  DataPackage.cpp
  Fifo.cpp
  STONNEModel.cpp
STONNE Tutorial @ASPLOS 2023

## Slide 26: STONNE Source files
STONNEModel.cpp drives the simulation based on the user configuration file
  1. The code reads the input file and selects the correct modules:
STONNE Tutorial @ASPLOS 2023

## Slide 27: STONNE Source files
STONNEModel.cpp drives the simulation based on the user configuration file
  2. After this, the class defines methods to load the layer, tile parameters, memory addresses and run the simulation. This is used to interface the simulator
STONNE Tutorial @ASPLOS 2023

## Slide 28: STONNE Source files
STONNEModel.cpp drives the simulation based on the user configuration file
  3. The code runs the cycle() method of each component until the execution is completed.
STONNE Tutorial @ASPLOS 2023

## Slide 29: Outline
Docker Image, Installation and overview of STONNE.
Hands-on #1: Simulating a real DNN on Flexible DNN Accelerators.
Hands-on #2: Simulating a DNN Layer on Flexagon using SST-STONNE.
Research use cases.
Conclusions.
STONNE Tutorial @ASPLOS 2023

## Slide 30: Objectives
1. Comprehensively understand how do flexible DNN architectures work.
2. Understand how to run simulations in STONNE using its STONNE User interface.
Understand how to run a real DNN in STONNE using the framework Pytorch.
STONNE Tutorial @ASPLOS 2023

## Slide 31: DNN benchmark
We will go through a real-life example to motivate our use case.
Application task: Image digit recognition
Benchmark: A Convolutional Neural Network (CNN).
Dataset: MNIST (60000 28x28-size images)
5
CNN
STONNE Tutorial @ASPLOS 2023

## Slide 32: CNN model
Layer | Operation | R | S | C | K | G | N | X | Y
0 | CONV | 5 | 5 | 1 | 16 | 1 | 1 | 32 | 32
1 | MaxPool | 2 | 2 | 16 | 16 | 1 | 1 | 28 | 28
2 | CONV | 5 | 5 | 16 | 32 | 1 | 1 | 18 | 18
3 | MaxPool | 2 | 2 | 32 | 32 | 1 | 1 | 14 | 14
4 | Dense | - | - | 1568 | 10 | - | - | - | -
STONNE Tutorial @ASPLOS 2023

## Slide 33: CNN model
Layer | Operation | R | S | C | K | G | N | X | Y
0 | CONV | 5 | 5 | 1 | 16 | 1 | 1 | 30 | 30
1 | MaxPool | 2 | 2 | 16 | 16 | 1 | 1 | 26 | 26
2 | CONV | 5 | 5 | 16 | 32 | 1 | 1 | 14 | 14
3 | MaxPool | 2 | 2 | 32 | 32 | 1 | 1 | 12 | 12
4 | Dense | - | - | 1568 | 10 | - | - | - | -
Simulated
Simulated
Simulated
STONNE Tutorial @ASPLOS 2023

## Slide 34: Simulated architecture
We will simulate our benchmark in a 64-MS MAERI architecture.
ID | Number of Multipliers | Distribution Bandwidth | Reduction Bandwidth
1 | 64 | 64 | 64
STONNE Tutorial @ASPLOS 2023

## Slide 35: Mapping the CNN onto the architectures
Given our CNN and our architecture, how do we map the computation?
STONNE Tutorial @ASPLOS 2023

## Slide 36: Mapping the CNN onto the architectures
Given our CNN and our two architectures, how do we map the computation?
  Answer: Tiling the layer.
STONNE Tutorial @ASPLOS 2023

## Slide 37: Mapping the CNN onto the architecture
Given our CNN and our two architectures, how do we map the computation?
Example: How do we map this layer?
R | S | C | K | G | N | X | Y | X' | Y'
2 | 2 | 3 | 2 | 1 | 1 | 4 | 4 | 3 | 3
T_R | T_S | T_C | T_K | T_G | T_N | T_X' | T_Y'
? | ? | ? | ? | ? | ? | ? | ?
Mapping?
STONNE Tutorial @ASPLOS 2023

## Slide 38: Mapping the CNN onto the architecture
Given our CNN and our two architectures, how do we map the computation?
Example: How do we map this layer?
R | S | C | K | G | N | X | Y | X' | Y'
2 | 2 | 3 | 2 | 1 | 1 | 4 | 4 | 3 | 3
T_R | T_S | T_C | T_K | T_G | T_N | T_X' | T_Y'
2 | 2 | 3 | 1 | 1 | 1 | 1 | 1
Mapping?
Virtual Neuron Size: ?
Number of Virtual Neurons: ?
STONNE Tutorial @ASPLOS 2023

## Slide 39: Mapping the CNN onto the architecture
Given our CNN and our two architectures, how do we map the computation?
Example: How do we map this layer?
R | S | C | K | G | N | X | Y | X' | Y'
2 | 2 | 3 | 2 | 1 | 1 | 4 | 4 | 3 | 3
T_R | T_S | T_C | T_K | T_G | T_N | T_X' | T_Y'
2 | 2 | 3 | 1 | 1 | 1 | 1 | 1
Mapping?
Virtual Neuron Size: 2*2*3=12
Number of Virtual Neurons: 1*1*1*1*1=1
STONNE Tutorial @ASPLOS 2023

## Slide 40: Mapping the CNN onto the architecture
Given our CNN and our two architectures, how do we map the computation?
Example: How do we map this layer?
R | S | C | K | G | N | X | Y | X' | Y'
2 | 2 | 3 | 2 | 1 | 1 | 4 | 4 | 3 | 3
T_R | T_S | T_C | T_K | T_G | T_N | T_X' | T_Y'
? | ? | ? | ? | ? | ? | ? | ?
Mapping?
Virtual Neuron Size: ?
Number of Virtual Neurons: ?
STONNE Tutorial @ASPLOS 2023

## Slide 41: Mapping the CNN onto the architecture
Given our CNN and our two architectures, how do we map the computation?
Example: How do we map this layer?
R | S | C | K | G | N | X | Y | X' | Y'
2 | 2 | 3 | 2 | 1 | 1 | 4 | 4 | 3 | 3
T_R | T_S | T_C | T_K | T_G | T_N | T_X' | T_Y'
2 | 2 | 1 | 2 | 1 | 1 | 1 | 1
Mapping?
Virtual Neuron Size: 2*2*1=4
Number of Virtual Neurons: 2*1*1*1*1=2
STONNE Tutorial @ASPLOS 2023

## Slide 42: Mapping the CNN onto the architecture
Given our CNN and our two architectures, how do we map the computation?
Example: How do we map this layer?
R | S | C | K | G | N | X | Y | X' | Y'
2 | 2 | 3 | 2 | 1 | 1 | 4 | 4 | 3 | 3
T_R | T_S | T_C | T_K | T_G | T_N | T_X' | T_Y'
? | ? | ? | ? | ? | ? | ? | ?
Mapping?
Virtual Neuron Size: ?
Number of Virtual Neurons: ?
STONNE Tutorial @ASPLOS 2023

## Slide 43: Mapping the CNN onto the architecture
Given our CNN and our two architectures, how do we map the computation?
Example: How do we map this layer?
R | S | C | K | G | N | X | Y | X' | Y'
2 | 2 | 3 | 2 | 1 | 1 | 4 | 4 | 3 | 3
T_R | T_S | T_C | T_K | T_G | T_N | T_X' | T_Y'
2 | 2 | 1 | 1 | 1 | 1 | 2 | 2
Mapping?
Virtual Neuron Size: 2*2*1=4
Number of Virtual Neurons: 1*1*1*2*2=4
STONNE Tutorial @ASPLOS 2023

## Slide 44: Mapping the CNN onto the architecture
Given our CNN and our two architectures, how do we map the computation?
Example: How do we map this layer?
K | M | N
4 | 2 | 1
T_K | T_M | T_N
? | ? | ?
Mapping?
Virtual Neuron Size: ?
Number of Virtual Neurons: ?
STONNE Tutorial @ASPLOS 2023

## Slide 45: Mapping the CNN onto the architecture
Given our CNN and our two architectures, how do we map the computation?
Example: How do we map this layer?
S | K | N
4 | 2 | 1
T_S | T_K | T_N
4 | 2 | 1
Mapping?
Virtual Neuron Size: 4
Number of Virtual Neurons: 2*1=2
S
K
STONNE Tutorial @ASPLOS 2023

## Slide 46: Mapping the CNN onto the architecture
Given our CNN and our architecture, how do we map the computation?
Layer | Operation | R | S | C | K | G | N | X | Y
0 | CONV | 5 | 5 | 1 | 16 | 1 | 1 | 32 | 32
1 | MaxPool | 2 | 2 | 16 | 16 | 1 | 1 | 28 | 28
2 | CONV | 5 | 5 | 16 | 32 | 1 | 1 | 18 | 18
3 | MaxPool | 2 | 2 | 32 | 32 | 1 | 1 | 14 | 14
Layer | Operation | S | K | N |  |  |  |  | 
4 | Dense | 1568 | 10 | 1 |  | - | - | - | -
Simulated
Simulated
Simulated
Number of Multipliers | DN BW | RN BW
64 | 64 | 64
STONNE Tutorial @ASPLOS 2023

## Slide 47: Mapping the CNN onto the architecture
Layer | Operation | R | S | C | K | G | N | X | Y
0 | CONV | 5 | 5 | 1 | 16 | 1 | 1 | 32 | 32
1 | MaxPool | 2 | 2 | 16 | 16 | 1 | 1 | 28 | 28
2 | CONV | 5 | 5 | 16 | 32 | 1 | 1 | 18 | 18
3 | MaxPool | 2 | 2 | 32 | 32 | 1 | 1 | 14 | 14
Layer | Operation | K | M | N |  |  |  |  | 
4 | Dense | 1568 | 10 | 1 |  | - | - | - | -
Simulated
Simulated
Simulated
Layer | Operation | T_R | T_S | T_C | T_K | T_G | T_N | T_X' | T_Y' | VN Size | # VNs | MSs used
0 | CONV | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?
2 | CONV | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?
Layer | Operation | T_S | T_K | T_N |  |  |  |  |  |  |  | 
4 | Dense | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?
Number of Multipliers | DN BW | RN BW
64 | 64 | 64
STONNE Tutorial @ASPLOS 2023

## Slide 48: Mapping the CNN onto the architecture
Layer | Operation | R | S | C | K | G | N | X | Y
0 | CONV | 5 | 5 | 1 | 16 | 1 | 1 | 32 | 32
1 | MaxPool | 2 | 2 | 16 | 16 | 1 | 1 | 28 | 28
2 | CONV | 5 | 5 | 16 | 32 | 1 | 1 | 18 | 18
3 | MaxPool | 2 | 2 | 32 | 32 | 1 | 1 | 14 | 14
Layer | Operation | K | M | N |  |  |  |  | 
4 | Dense | 1568 | 10 | 1 |  | - | - | - | -
Simulated
Simulated
Simulated
Layer | Operation | T_R | T_S | T_C | T_K | T_G | T_N | T_X' | T_Y' | VN Size | # VNs | MSs used
0 | CONV | 5 | 5 | 1 | 2 | 1 | 1 | 1 | 1 | 25 | 2 | 50
2 | CONV | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?
Layer | Operation | T_S | T_K | T_N |  |  |  |  |  |  |  | 
4 | Dense | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?
Number of Multipliers | DN BW | RN BW
64 | 64 | 64
STONNE Tutorial @ASPLOS 2023

## Slide 49: Mapping the CNN onto the architecture
Layer | Operation | R | S | C | K | G | N | X | Y
0 | CONV | 5 | 5 | 1 | 16 | 1 | 1 | 32 | 32
1 | MaxPool | 2 | 2 | 16 | 16 | 1 | 1 | 28 | 28
2 | CONV | 5 | 5 | 16 | 32 | 1 | 1 | 18 | 18
3 | MaxPool | 2 | 2 | 32 | 32 | 1 | 1 | 14 | 14
Layer | Operation | K | M | N |  |  |  |  | 
4 | Dense | 1568 | 10 | 1 |  | - | - | - | -
Simulated
Simulated
Simulated
Layer | Operation | T_R | T_S | T_C | T_K | T_G | T_N | T_X' | T_Y' | VN Size | # VNs | MSs used
0 | CONV | 5 | 5 | 1 | 2 | 1 | 1 | 1 | 1 | 25 | 2 | 50
2 | CONV | 1 | 1 | 16 | 4 | 1 | 1 | 1 | 1 | 16 | 4 | 64
Layer | Operation | T_S | T_K | T_N |  |  |  |  |  |  |  | 
4 | Dense | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?
Number of Multipliers | DN BW | RN BW
64 | 64 | 64
STONNE Tutorial @ASPLOS 2023

## Slide 50: Mapping the CNN onto the architecture
Layer | Operation | R | S | C | K | G | N | X | Y
0 | CONV | 5 | 5 | 1 | 16 | 1 | 1 | 32 | 32
1 | MaxPool | 2 | 2 | 16 | 16 | 1 | 1 | 28 | 28
2 | CONV | 5 | 5 | 16 | 32 | 1 | 1 | 18 | 18
3 | MaxPool | 2 | 2 | 32 | 32 | 1 | 1 | 14 | 14
Layer | Operation | K | M | N |  |  |  |  | 
4 | Dense | 1568 | 10 | 1 |  | - | - | - | -
Simulated
Simulated
Simulated
Layer | Operation | T_R | T_S | T_C | T_K | T_G | T_N | T_X' | T_Y' | VN Size | # VNs | MSs used
0 | CONV | 5 | 5 | 1 | 2 | 1 | 1 | 1 | 1 | 25 | 2 | 50
2 | CONV | 1 | 1 | 16 | 4 | 1 | 1 | 1 | 1 | 16 | 4 | 64
Layer | Operation | T_S | T_K | T_N |  |  |  |  |  |  |  | 
4 | Dense | 32 | 2 | 1 | - | - | - | - | - | 32 | 2 | 64
Number of Multipliers | DN BW | RN BW
64 | 64 | 64
STONNE Tutorial @ASPLOS 2023

## Slide 51: Simulating using the STONNE User interface
Before running the real benchmark we will use the STONNE User interface to simulate our layers.
This will run the layers with the correct dimensions but using random data.
STONNE Tutorial @ASPLOS 2023

## Slide 52: Simulating using the STONNE User interface
Once the simulation has finished we can get the energy and area numbers:
Statistics.json
Statistics.counters
Energy
Table-Based Model
Energy
Chip Area
Statistics.counters
Area
Table-Based Model
STONNE Tutorial @ASPLOS 2023

## Slide 53: Simulating using the STONNE User interface
Script to calculate the energy and area numbers:
  /home/stonne_omega:
    omega
    stonne:
      ASPLOS22
      pytorch-frontend
        stonne_connection
      stonne:
        stonne.elf
        Include
        src
        external
        stonne_linker_src
        energy_tables
          calculate_energy.py
          energy_model.txt
STONNE Tutorial @ASPLOS 2023

## Slide 54: Simulating using the STONNE User interface
Syntax: ./calculate_energy [-v] -table_file=<Energy&Area table> -counter_file=<counter stats> -out_file=<output file name>
STONNE Tutorial @ASPLOS 2023

## Slide 55: Simulating using the Pytorch interface
Our image digit recognition benchmark is located in /home/stonne_omega/stonne/ASPLOS22/handson-1
  train_dnn.py: Used to train our CNN and get the trained weights.
  evaluate_dnn.py: Used to evaluate the accuracy of our CNN.
  dnn.py: Defines our CNN.
  deployment.py: This is the final file which is used to predict real images.
STONNE Tutorial @ASPLOS 2023

## Slide 56: Simulating using the Pytorch interface
Steps towards CPU execution:
  1. Run train_dnn.py script to obtain the weights.
  2. Run evaluate_dnn.py to measure the accuracy of the network.
  3. Run deployment.py
STONNE Tutorial @ASPLOS 2023

## Slide 57: Simulating using the Pytorch interface
Steps towards CPU execution:
  1. Run train_dnn.py script to obtain the weights.
  2. Run evaluate_dnn.py to measure the accuracy of the network.
  3. Run deployment.py
STONNE Tutorial @ASPLOS 2023

## Slide 58: Simulating using the Pytorch interface
Once we have tested the inference procedure on the CPU, let's run it in our simulated accelerator.
Steps towards simulation:
  1. Set up the hardware configuration file.
  2. Set up the tile configuration files
  3. Change the CONV and Linear operations in order to simulate them.
STONNE Tutorial @ASPLOS 2023

## Slide 59: STONNE Mapper
New version of STONNE also includes a mapper to autogenerate the best tile.
Developer of STONNE mapper: Adrián fenollar navarro from the University of Murcia (Contact: adrian.fenollarn@um.es)
STONNE Tutorial @ASPLOS 2023

## Slide 60: STONNE Mapper
STONNE Mapper usage:
  From Pytorch:
  From STONNE User Interface:
    BEFORE (still compatible): ./stonne -CONV -R=3 -S=3 -C=6 -G=1 -K=6 -N=1 -X=20 -Y=20 -T_R=3 -T_S=3 -T_C=1 -T_G=1 -T_K=1 -T_N=1 -T_X_=3 -T_Y_=1 -num_ms=64 -dn_bw=8
    Today: ./stonne -CONV -R=3 -S=3 -C=6 -G=1 -K=6 -N=1 -X=20 -Y=20 -generate_tile=energy -num_ms=64 -dn_bw=8 -rn_bw=8 -accumulation_buffer=1
Tile_file.txt
STONNE Tutorial @ASPLOS 2023

## Slide 61: Agenda
Time (PT) | Topic | Presenter
1:40 – 2:00 | Flexible Accelerators | José L. Abellán
2:00 – 2:20 | Cycle accurate simulation and Overview of STONNE | José L. Abellán
2:20 – 3:20 | (Hands-on) STONNE | Francisco Muñoz-Martínez
3:20 – 3:40 | Coffee Break | 
3:40 – 4:10 | (Hands-on) SST-STONNE | Francisco Muñoz-Martínez
4:10 – 4:40 | (Hands-on) OMEGA | Raveesh Garg
4:40 – 5:00 | Roadmap and Concluding Remarks | Tushar Krishna
https://stonne-simulator.github.io/ASPLOSTUT.html

## Slide 62: Outline
Docker Image, Installation and overview of STONNE.
Hands-on #1: Simulating a real DNN on Flexible DNN Accelerators.
Hands-on #2: Simulating a DNN Layer on Flexagon using SST-STONNE.
Research use cases.
Conclusions.
STONNE Tutorial @ASPLOS 2023

## Slide 63: SST-STONNE
STONNE simulator does not model a proper memory hierarchy (only datapath).
  See stonne/src/SDMemory.cpp
  See stonne/src/SparseSDMemory.cpp
STONNE Tutorial @ASPLOS 2023

## Slide 64: SST-STONNE
To improve this, we have integrated STONNE into SST simulator, creating SST-STONNE
https://github.com/stonne-simulator/sst-elements-with-stonne
STONNE Tutorial @ASPLOS 2023

## Slide 65: Docker image
Project organization:
  /SST-STONNE:
    src:
      sst-core
        ...
      Sst-elements-with-stonne:
        src/sst/elements/sstStonne
          stonne_linker_src
          src
          Tests
          Makefile
STONNE Tutorial @ASPLOS 2023

## Slide 66: SST-STONNE
In this implementation the memory controllers send packets to memHierarchy simulator within SST.
  See /SST-STONNE/src/sst-elements-with-stonne/src/sst/elements/sstStonne/src/SDMemory.cpp (inner
STONNE Tutorial @ASPLOS 2023

## Slide 67: SpMSpM operation
Sparsity in matrices is an emerging trend in modern DNN workloads.
STONNE Tutorial @ASPLOS 2023

## Slide 68: SpMSpM operation
Exploiting sparsity is done via the SpMSpM operation (Sparse-Sparse Matrix Multiplication).
STONNE Tutorial @ASPLOS 2023

## Slide 69: SpMSpM operation dataflows
The SpMSpM operation may be executed using three dataflows:
STONNE Tutorial @ASPLOS 2023

## Slide 70: SpMSpM operation dataflows
The SpMSpM operation may be executed using three dataflows (6 variants):
STONNE Tutorial @ASPLOS 2023

## Slide 71: SpMSpM accelerators
SpMSpM state-of-the-art accelerators implements one dataflow.
STONNE Tutorial @ASPLOS 2023

## Slide 72: SpMSpM accelerators
However, the optimal dataflow changes from a DNN to another, and even within a DNN model, from one layer to another.
STONNE Tutorial @ASPLOS 2023

## Slide 73: Flexagon
To fill this gap, we have proposed Flexagon, the first accelerator supporting the three dataflows.
Flexagon will be presented on ASPLOS 2023 on Tuesday at session 4C.
STONNE Tutorial @ASPLOS 2023

## Slide 74: Flexagon
Flexagon is implemented in SST-STONNE by implementing three memory controllers and a new reduction/merging (MRN) network.
Reference for Inner-Product in SparseSDMemory.cpp
Reference for Outer-Product in OuterLoopSpGEMMSDMemory.cpp
Reference for Gustavson's in GustavsonsSpGEMMSDMemory.cpp
Reference for MRN: SparseFlex_ASNetwork.cpp
STONNE Tutorial @ASPLOS 2023

## Slide 75: Flexagon
Let's run Flexagon!
STONNE Tutorial @ASPLOS 2023

## Slide 76: Outline
Docker Image, Installation and overview of STONNE.
Hands-on #1: Simulating a real DNN on Flexible DNN Accelerators.
Hands-on #2: Using STONNE to evaluate a research use case – Exploiting sparsity.
Hands-on #3: Simulating a DNN Layer on Flexagon using SST-STONNE.
Research use cases.
Conclusions.
STONNE Tutorial @ASPLOS 2023

## Slide 77: Use case #1: STIFT
We can use STONNE to create and evaluate new architectural modules for ML accelerators.
STIFT [Francisco Munoz-Martinez et. al., NOCS21]
STONNE Tutorial @ASPLOS 2023

## Slide 78: Use case #2: Sparse filters scheduling
We can use STONNE to evaluate new compilation techniques such as sparse scheduling.
STONNE [Francisco Munoz-Martinez et. al., IISWC21]
STONNE Tutorial @ASPLOS 2023

## Slide 79: Outline
Docker Image, Installation and overview of STONNE.
Hands-on #1: Simulating a real DNN on Flexible DNN Accelerators.
Hands-on #2: Using STONNE to evaluate a research use case – Exploiting sparsity.
Hands-on #3: Simulating a DNN Layer on Flexagon using SST-STONNE.
Research use cases.
Conclusions.
STONNE Tutorial @ASPLOS 2023

## Slide 80: Conclusions
STONNE is a cycle-accurate simulator for ML accelerators.
During this hands-on we have seen:
  How to use the STONNE user interface to run synthetic operations.
  How to use the Pytorch interface to run end-to-end models with STONNE.
  How to use SST-STONNE to run Flexagon accelerator (attend our session 5C!!)
Find STONNE on http://github.com/stonne_simulator/stonne
Find SST-STONNE on https://github.com/stonne-simulator/sst-elements-with-stonne
STONNE Tutorial @ASPLOS 2023

## Slide 81: Acknowledgements
Co-Design Center for Artificial Intelligence-Focused Architectures and Algorithms Funded By

## Slide 82: Hands-on
Francisco Muñoz-Martínez
francisco.munoz2@um.es
Universidad de Murcia (UM)