## Slide 1: A Simulation TOol for Neural Network Engines
José L. Abellán, PhD
jlabellan@um.es
University of Murcia

## Slide 2: Agenda
Time (PT) | Topic | Presenter
1:40 – 2:00 | Flexible Accelerators | José L. Abellán
2:00 – 2:20 | Cycle accurate simulation and Overview of STONNE | José L. Abellán
2:20 – 3:20 | (Hands-on) STONNE | Francisco Muñoz-Martínez
3:20 – 3:40 | Coffee Break | 
3:40 – 4:10 | (Hands-on) SST-STONNE | Francisco Muñoz-Martínez
4:10 – 4:40 | (Hands-on) OMEGA | Raveesh Garg
4:40 – 5:00 | Roadmap and Concluding Remarks | Tushar Krishna
https://stonne-simulator.github.io/ASPLOSTUT.html

## Slide 3: Outline
Motivation
STONNE Framework
Validation
Uses Cases of STONNE
Conclusions

## Slide 4: Outline
Motivation
STONNE Framework
Validation
Uses Cases of STONNE
Conclusions

## Slide 5: Cycle-level Architectural Simulation
Architectural Design Ideas
RTL Design
Physical Design
Verification
Manufacture
Chip-Designing Process
Architectural Design Ideas
High-level Lang. Design (e.g., C++)
Simulator Implementation
SW Testing
Architectural Simulation
Accurate Architectural Design Prototyping!
1
2

## Slide 6: Cycle-level Architectural Simulators
Microarchitectural simulators have been extensively used during the design process of CPUs (Gem5) and GPUs (MGPUSim)
However, how can we simulate the wide diversity of DNN accelerators (i.e., rigid, flexible and data-dependent optimizations)?
  We need cycle-level simulation.
  We need to support flexible (dense and sparse) and rigid accelerators.
  We need to perform end-to-end simulation.

## Slide 7: Cycle-level Architectural Simulators
Microarchitectural simulators have been extensively used during the design process of CPUs (Gem5) and GPUs (MGPUSim)
However, how can we simulate the wide diversity of DNN accelerators (i.e., rigid, flexible and data-dependent optimizations)?
  We need cycle-level simulation.
  We need to support flexible (dense and sparse) and rigid accelerators.
  We need to perform end-to-end simulation.
STONNE (A Simulation Tool for Neural Network Engines)

## Slide 8: Cycle-level Architectural Simulators
Microarchitectural simulators have been extensively used during the design process of CPUs (Gem5) and GPUs (MGPUSim)
However, how can we simulate the wide diversity of DNN accelerators (i.e., rigid, flexible and data-dependent optimizations)?
  We need cycle-level simulation.
  We need to support flexible (dense and sparse) and rigid accelerators.
  We need to perform end-to-end simulation.
DOG (0.9), CAT (0.09), BIRD (0.01)
AREA

## Slide 9: Why another simulator for DNN accelerators?

## Slide 10: Why another simulator for DNN accelerators?
State-of-the-art Simulators for DNN Accelerators
F. Muñoz-Martínez, J. L. Abellán, M. E. Acacio and T. Krishna, "STONNE: Enabling Cycle-Level Microarchitectural Simulation for DNN Inference Accelerators”. Proc. of IISWC 2021.​

## Slide 11: Why another simulator for DNN accelerators?
State-of-the-art Simulators for DNN Accelerators
RTL implementations are
slow to modify
F. Muñoz-Martínez, J. L. Abellán, M. E. Acacio and T. Krishna, "STONNE: Enabling Cycle-Level Microarchitectural Simulation for DNN Inference Accelerators”. Proc. of IISWC 2021.​

## Slide 12: Why another simulator for DNN accelerators?
State-of-the-art Simulators for DNN Accelerators
Analytical models are not accurate for complex designs
F. Muñoz-Martínez, J. L. Abellán, M. E. Acacio and T. Krishna, "STONNE: Enabling Cycle-Level Microarchitectural Simulation for DNN Inference Accelerators”. Proc. of IISWC 2021.​

## Slide 13: Why another simulator for DNN accelerators?
Cycle-level simulation is required to faithfully model complex DNN architectures
F. Muñoz-Martínez, J. L. Abellán, M. E. Acacio and T. Krishna, "STONNE: Enabling Cycle-Level Microarchitectural Simulation for DNN Inference Accelerators”. Proc. of IISWC 2021.​

## Slide 14: Outline
Motivation
STONNE Framework
Validation
Uses Cases of STONNE
Conclusions

## Slide 15: STONNE Framework
STONNE is a cycle-level microarchitectural simulator written in C++ for DNN inference accelerators.
Open-Sourced under the MIT License:
  https://github.com/stonne-simulator/stonne
STONNE is composed of 3 main building blocks:

## Slide 16: Input Module
STONNE is a cycle-level microarchitectural simulator written in C++ for DNN inference accelerators.
Open-Sourced under the MIT License:
  https://github.com/stonne-simulator/stonne
STONNE is composed of 3 main building blocks:

## Slide 17: Input Module
STONNE User Interface: A command line that the user can use to run an instance of the simulator with random input values.

## Slide 18: Input Module
PyTorch Framework: We integrate Pytorch with STONNE so that instances of operations are off-loaded to the simulator.

## Slide 19: Input Module
PyTorch Framework: We integrate Pytorch with STONNE so that instances of operations are off-loaded to the simulator.

## Slide 20: Input Module
PyTorch Framework: We integrate Pytorch with STONNE so that instances of operations are off-loaded to the simulator.

## Slide 21: Output Module
STONNE is a cycle-level microarchitectural simulator written in C++ for DNN inference accelerators.
Open-Sourced under the MIT License:
  https://github.com/stonne-simulator/stonne
STONNE is constituted by 3 main building blocks:

## Slide 22: Output Module
This module reports simulation statistics such as performance, compute unit utilization, and activity counts of different components such as wires, FIFOs or SRAM usage.
"MSNetworkStats" : {
"MSwitchStats" : [
{
"Total_cycles" : 396168,
"Idle_cycles" : 1896,
"N_multiplications" : 394272,
"N_input_forwardings_send" : 0,
"N_input_forwardings_receive" : 392496,
"N_inputs_receive_from_memory" : 1776,
"N_weights_receive_from_memory" : 8,
"N_weight_fifo_flush" : 7,
"N_psums_receive" : 0,
"N_psum_forwarding_send" : 0,
"N_configurations" : 1
,"ActivationFifo" : {
"N_pops" : 1776,
"N_pushes" : 1776,
"N_fronts" : 0,
"Max_occupancy" : 1
…..
Statistics.json
[MSNetwork]
MN_WIRE WRITE=392496 READ=0
MN_WIRE WRITE=392496 READ=0
MN_WIRE WRITE=0 READ=0
MN_WIRE WRITE=392496 READ=0
MN_WIRE WRITE=392496 READ=0
MN_WIRE WRITE=0 READ=0
MN_WIRE WRITE=392496 READ=0
MN_WIRE WRITE=392496 READ=0
MN_WIRE WRITE=0 READ=0
MN_WIRE WRITE=392496 READ=0
MN_WIRE WRITE=392496 READ=0
[GlobalBuffer]
GLOBALBUFFER READ=3582144 WRITE=3154176
….
Statistics.counters

## Slide 23: Output Module
This module reports simulation statistics such as performance, compute unit utilization, and activity counts of different components such as wires, FIFOs or SRAM usage.
Statistics.json
Statistics.counters
Energy
Table-Based Model
Energy
Chip Area
Statistics.counters
Area
Table-Based Model
AREA

## Slide 24: Simulation Platform
STONNE is a cycle-level microarchitectural simulator written in C++ for DNN inference accelerators.
Open-Sourced under the MIT License:
  https://github.com/stonne-simulator/stonne
STONNE is constituted by 3 main building blocks:

## Slide 25: STONNE API, Mapper and Configuration Unit
Instruction | Description
CreateInstance | Creates an instance of STONNE
ConfigureCONV | Configures the accelerator to run a convolution operation
ConfigureLinear | Configures the accelerator to run a fully-connected layer
ConfigureDMM | Configures the accelerator to run a matrix multiplication
ConfigureSpMM | Configures the accelerator to run a sparse matrix multipl.
ConfigureMaxPool | Configures the accelerator to run a max pooling layer
ConfigureData | Configures weights, input and outputs addresses from the CPU to the accelerator memory
RunOperation | Launches the simulation according to the current configuration of the architecture
The Mapper generates a set of signals based on the tile and layer parameters (i.e., it determines the required signals to configure the virtual neurons).
The Configuration Unit delivers the signals to the simulation engine, configuring the hardware.

## Slide 26: Simulation Engine
Most current DNN accelerator architectures can be logically organized as three configurable network fabrics:
  Distribution Network
  Multiplier Network
  Reduction Network

## Slide 27: Simulation Engine

## Slide 28: Simulation Engine

## Slide 29: Simulation Engine

## Slide 30: Simulation Engine

## Slide 31: Outline
Motivation
STONNE Framework
Validation
Uses Cases of STONNE
Conclusions

## Slide 32: Validation
We have validated three state-of-the-art accelerators (i.e., MAERI, SIGMA and TPU) modeled with STONNE against their RTL implementations.
Max 3.10% of difference in terms of number of cycles (1.5% on average)

## Slide 33: Outline
Motivation
STONNE Framework
Validation
Uses Cases of STONNE
Conclusions
F. Muñoz-Martínez, J. L. Abellán, M. E. Acacio and T. Krishna, "STONNE: Enabling Cycle-Level Microarchitectural Simulation for DNN Inference Accelerators”. Proc. of IISWC 2021.

## Slide 34: UC#1: DNN inference in TPU, MAERI and SIGMA
Aim: Demonstrate how STONNE can be used to conduct comprehensive evaluations of several DNN accelerators running complete DNN models
Simulated Accelerators: TPU, MAERI, SIGMA with 256 MSs and 128 elem/cycle BW
TPU-like
MAERI-like
SIGMA-like

## Slide 35: UC#1: DNN inference in TPU, MAERI and SIGMA
Benchmarks:

## Slide 36: UC#1: DNN inference in TPU, MAERI and SIGMA
Results: Number of cycles

## Slide 37: UC#1: DNN inference in TPU, MAERI and SIGMA
Results: Number of cycles
MAERI-like architecture 20% faster than the TPU-like architecture

## Slide 38: UC#1: DNN inference in TPU, MAERI and SIGMA
Results: Number of cycles
MAERI-like architecture 20% faster than the TPU-like architecture
SIGMA-like architecture is 91% faster than a MAERI-like one

## Slide 39: UC#2: Data-Dependent HW Optimizations
Aim: Prove how the back-end of STONNE can be easily extended to model data-dependent accelerators
Simulated Accelerator: SnaPea

## Slide 40: UC#2: Data-Dependent HW Optimizations
Implementation:
TPU-like

## Slide 41: UC#2: Data-Dependent HW Optimizations
Implementation:
Negative detection Logic
if(current_output < 0):
result = 0;
else:
continue();

## Slide 42: UC#2: Data-Dependent HW Optimizations
Implementation:
Order weights
order_weights(weights)
off_load_simulation();
if(current_output < 0):
result = 0;
else:
continue();
Negative detection Logic

## Slide 43: UC#2: Data-Dependent HW Optimizations
Parameters: 64 MSs and ASs, and 64 elements/cycle GB read/write BW
Benchmarks: Pure CNN models

## Slide 44: UC#2: Data-Dependent HW Optimizations
Results:

## Slide 45: UC#2: Data-Dependent HW Optimizations
Results:
Average SpeedUp of 35%
Average Energy Savings of 21%

## Slide 46: Outline
Motivation
STONNE Framework
Validation
Uses Cases of STONNE
Conclusions

## Slide 47: Conclusions
As the complexity of the microarchitecture of DNN accelerators grows, the analytical models are not able to capture many important subtleties that simulation at cycle level does.
STONNE is an accurate cycle-level simulator for next-generation DNN accelerator architectures.
STONNE can model rigid, flexible and data-dependent accelerators performing actual computation.
https://github.com/stonne-simulator/stonne
F. Muñoz-Martínez, J. L. Abellán, M. E. Acacio and T. Krishna, "STONNE: Enabling Cycle-Level Microarchitectural Simulation for DNN Inference Accelerators”. Proc. of IISWC 2021.

## Slide 48: Acknowledgements
Co-Design Center for Artificial Intelligence-Focused Architectures and Algorithms Funded By

## Slide 49: A Simulation TOol for Neural Network Engines
José L. Abellán, PhD
jlabellan@ucam.edu
Universidad Católica de Murcia (UCAM)

## Slide 50: UC#1: DNN inference in TPU, MAERI and SIGMA
Results: Energy
SIGMA-like architecture is 70% and 54% more energy efficient than the MAERI-like and TPU-like architectures

## Slide 51: UC#1: DNN inference in TPU, MAERI and SIGMA
Results: Area
The differences in area are not as noticeable as those in the energy and runtime metrics.
Area dominated by the SRAM (i.e., GB): 70%, 77% and 82% of the total area of the MAERI-like, SIGMA-like and TPU-like architectures.

## Slide 52: UC#2: Data-Dependent HW Optimizations
Results:

## Slide 53: UC#2: Data-Dependent HW Optimizations
Results:
30% reduction of # of operations
16 % reduction of # of Memory Accesses

## Slide 54: UC#3: Filter Scheduling in Sparse Accelerators
Aim: Demonstrate that precise, full-model evaluation is required to expose the particular values used during inference
Motivation and Idea: The way in which the filters of a sparse DNN model are scheduled onto a DNN inference accelerator might have significant impact on performance

## Slide 55: UC#3: Filter Scheduling in Sparse Accelerators
Aim: Demonstrate that precise, full-model evaluation is required to expose the particular values used during inference
Motivation and Idea: The way in which the filters of a sparse DNN model are scheduled onto a DNN inference accelerator might have significant impact on performance

## Slide 56: UC#3: Filter Scheduling in Sparse Accelerators
Aim: Demonstrate that precise, full-model evaluation is required to expose the particular values used during inference
Motivation and Idea: The way in which the filters of a sparse DNN model are scheduled onto a DNN inference accelerator might have significant impact on performance

## Slide 57: UC#3: Filter Scheduling in Sparse Accelerators
Aim: Demonstrate that precise, full-model evaluation is required to expose the particular values used during inference
Motivation and Idea: The way in which the filters of a sparse DNN model are scheduled onto a DNN inference accelerator might have significant impact on performance

## Slide 58: UC#3: Filter Scheduling in Sparse Accelerators
Aim: Demonstrate that precise, full-model evaluation is required to expose the particular values used during inference
Motivation and Idea: The way in which the filters of a sparse DNN model are scheduled onto a DNN inference accelerator might have significant impact on performance

## Slide 59: UC#3: Filter Scheduling in Sparse Accelerators
Aim: Demonstrate that precise, full-model evaluation is required to expose the particular values used during inference
Motivation and Idea: The way in which the filters of a sparse DNN model are scheduled onto a DNN inference accelerator might have significant impact on performance

## Slide 60: UC#3: Filter Scheduling in Sparse Accelerators
Aim: Demonstrate that precise, full-model evaluation is required to expose the particular values used during inference
Motivation and Idea: The way in which the filters of a sparse DNN model are scheduled onto a DNN inference accelerator might have significant impact on performance

## Slide 61: UC#3: Filter Scheduling in Sparse Accelerators
Implementation:
SIGMA-like

## Slide 62: UC#3: Filter Scheduling in Sparse Accelerators
Implementation:
SIGMA-like
We do not require
modifications in the accelerator

## Slide 63: UC#3: Filter Scheduling in Sparse Accelerators
Implementation:
SIGMA-like
We do not require
modifications in the accelerator

## Slide 64: UC#3: Filter Scheduling in Sparse Accelerators
Implementation:
SIGMA-like
Pre-simulation function to order the filters based on a certain heuristic
We do not require
modifications in the accelerator

## Slide 65: UC#3: Filter Scheduling in Sparse Accelerators
Implementation: We implement two heuristic algorithms:
  Largest Filter First (LFF): The filters are reordered so that the sparse controller always selects the largest available filter.
  Random (RDM): The filters are reordered randomly.
  No Schedule (NS): The filters are selected as they are in the model.

## Slide 66: UC#3: Filter Scheduling in Sparse Accelerators
Simulated Parameters: SIGMA-like architecture with 256 multipliers and adders and 128 elements/cycle Global Buffer(GB) read/write bandwidth.
Benchmarks:

## Slide 67: UC#3: Filter Scheduling in Sparse Accelerators
Results:

## Slide 68: UC#3: Filter Scheduling in Sparse Accelerators
Results:
LFF obtains performance benefits
of up to 11% (7% on average).

## Slide 69: UC#3: Filter Scheduling in Sparse Accelerators
Results:
RDM does not translate into better performance.
LFF obtains performance benefits
of up to 11% (7% on average).

## Slide 70: UC#3: Filter Scheduling in Sparse Accelerators
Results:

## Slide 71: UC#3: Filter Scheduling in Sparse Accelerators
Results:
Low-Sensitive layers: Do not represent performance benefit at all

## Slide 72: UC#3: Filter Scheduling in Sparse Accelerators
Results:
High-Sensitive layers: Up to 36% performance gain

## Slide 73: UC#3: Filter Scheduling in Sparse Accelerators
Results:
Medium-Sensitive layers: Up to 17% performance gain