## Slide 1: Understanding the Design Space of Sparse/Dense Multiphase Dataflows for Mapping Graph Neural Networks on Spatial Accelerators
Raveesh Garg1, Eric Qin1, Francisco Muñoz-Martínez2, Robert Guirado3, Akshay Jain4, Sergi Abadal3, José L. Abellán2, Manuel E. Acacio2, Eduard Alarcón3, Sivasankaran Rajamanickam6, Tushar Krishna1
1Georgia Tech, 2Universidad de Murcia, 3Universitat Politecnica de Catalunya,
4Neutroon, 6Sandia National Laboratories
*This work is accepted for publication to IPDPS 2022. Preprint- https://arxiv.org/abs/2103.07977
Notes: Intro, title, collaboration b/w 6 unis
Transition: Deep Learning and graph representation

## Slide 2: Agenda
Time (PT) | Topic | Presenter
1:40 – 2:00 | Flexible Accelerators | José L. Abellán
2:00 – 2:20 | Cycle accurate simulation and Overview of STONNE | José L. Abellán
2:20 – 3:20 | (Hands-on) STONNE | Francisco Muñoz-Martínez
3:20 – 3:40 | Coffee Break | 
3:40 – 4:10 | (Hands-on) SST-STONNE | Francisco Muñoz-Martínez
4:10 – 4:40 | (Hands-on) OMEGA | Raveesh Garg
4:40 – 5:00 | Roadmap and Concluding Remarks | Tushar Krishna
https://stonne-simulator.github.io/ASPLOSTUT.html

## Slide 3: Outline
Graph Neural Networks (GNNs)
GNN Dataflows – Taxonomy and modeling
Hands-on exercises

## Slide 4: Learning on Irregular Data
Biochemistry
Social Networks
Irregular Data
Regular Data
Notes: Deep Learning -> success in Computer vision  regular.  every pixel has the same set of neighbours and the same filter can slide uniformly
Real world data irregular and unstructured  captured by graphs

## Slide 5: Graph Neural Networks
2
1
3
5
4
Graph
6
2
1
3
5
4
6
Aggregation phase
Aggregation of neighboring feature vectors, for example, v4=v3+v6
Combination phase
2
1
3
5
4
6
This is a feature transformation phase feature vector of each vertex is transformed using trained weights similar to NN.
Notes: GNN successirregular data
Aggregation and Combination mainly

## Slide 6: GNN Computations
Graphs can also be represented as adjacency matrix with non-zeros representing the connection as shown.
Thus, Aggregation phase becomes an SpMM problem and Combination involves DenseGEMMs
V: Vertices; N: Neighbors; F: Input Features, G: Output Features
Notes: (on slides where used)

## Slide 7: Key characteristics of GNNs
Aggregation and Combination phases
Interplay of sparse and dense computations.
Reuse opportunities between the two phases.
Squares the design-space.
Complicates it further due to dependency between the phases.
GNNs offer reuse opportunities between two phases which makes the design-space of dataflows and mappings more complex.

## Slide 8: Outline
Graph Neural Networks (GNNs)
GNN Dataflows – Taxonomy and modeling
Hands-on Exercises

## Slide 9: Intra-phase dataflows
Intra-phase dataflows represent dataflows within a phase
As discussed before, individual dataflows consist of loop orders (VGF) and parallelization strategies (V and G parallel)
V: Vertices; N: Neighbors; F: Input Features, G: Output Features
for(int v=0;v<V;v+=T_V)
for(int g=0;g<G;g+=T_G)
for(int f=0;f<F;f+=T_F)
parfor(int v1=0;v1<T_V;v1++) //parallel
parfor(int g1=0;g1<T_G;g1++) //parallel
parfor(int f1=0;f1<T_F;f1++) //parallel
X1[v+v1][g+g1]+=I[v+v1][f+f1]*W[f+f1][g+g1];
Loop order - VGF (V→ G→ F )
Tile size determines spatial or temporal.
s⇒ Spatial⇒ T_Dim>1 and
t⇒ Temporal⇒ T_Dim=1
Example: T_V=2, T_G=2, T_F=1
V and G have spatial parallelism (s) and F is temporal (t)
Example: VsGsFt
F
Tile
Intermediate matrix
W
X1
Notes: After first bullet. This figure shows some of the loop transformations that can be done in a matrix dataflow.
****animation****

## Slide 10: Inter-phase Dataflows
Inter-phase dataflows describe the data reuse strategies between the two phases. We classify them into 3 categories
Sequential (SEQ)
Sequential Pipeline (SP)
Parallel Pipeline (PP)

## Slide 11: Execution of SEQ dataflows
Accelerator
PE running Aggregation
PE running Combination

## Slide 12: Execution of SEQ dataflows
Accelerator
Matrix multiplications
V: Vertices; N: Neighbors; F: Input Features, G: Output Features
PE running Aggregation
PE running Combination

## Slide 13: Execution of SEQ dataflows
WR
Occupancy of the intermediate matrix inside the buffer =
Accelerator
Matrix multiplications
Inside the global buffer/memory hierarchy
V: Vertices; N: Neighbors; F: Input Features, G: Output Features
PE running Aggregation
PE running Combination

## Slide 14: Execution of SEQ dataflow
RD
Occupancy of the intermediate matrix inside the buffer =
Accelerator
Matrix multiplications
Inside the global buffer/memory hierarchy
V: Vertices; N: Neighbors; F: Input Features, G: Output Features
PE running Aggregation
PE running Combination

## Slide 15: Execution example of SP dataflow
Here, step refers to the duration in which producer writes a part of the intermediate matrix and consumer reads a part of the intermediate matrix
Assuming that the computations are staged row-wise.
WR
Occupancy of the intermediate matrix inside the buffer =
Accelerator
Matrix multiplications
Inside the global buffer
V: Vertices; N: Neighbors; F: Input Features, G: Output Features

## Slide 16: Execution example of SP dataflow
RD
Occupancy of the intermediate matrix inside the buffer =
Accelerator
Matrix multiplications
Inside the global buffer
V: Vertices; N: Neighbors; F: Input Features, G: Output Features

## Slide 17: Execution example of SP dataflow
WR
Occupancy of the intermediate matrix inside the buffer =
Accelerator
Matrix multiplications
Inside the global buffer
V: Vertices; N: Neighbors; F: Input Features, G: Output Features

## Slide 18: Execution example of SP dataflow
RD
Occupancy of the intermediate matrix inside the buffer =
Accelerator
Matrix multiplications
Inside the global buffer
V: Vertices; N: Neighbors; F: Input Features, G: Output Features

## Slide 19: Execution example of PP dataflow
Here, step refers to the duration in which producer writes a part of the intermediate matrix and consumer reads a part of the intermediate matrix
Assuming that the computations are staged row-wise.
WR
Occupancy of the intermediate matrix inside the buffer =
Accelerator
Matrix multiplications
Inside the global buffer
V: Vertices; N: Neighbors; F: Input Features, G: Output Features
Notes: Animate With and without matrix

## Slide 20: Execution example of PP dataflow
Here, step refers to the duration in which producer writes a part of the intermediate matrix and consumer reads a part of the intermediate matrix
WR
RD
Occupancy of the intermediate matrix inside the buffer =
Accelerator
Matrix multiplications
Inside the global buffer
V: Vertices; N: Neighbors; F: Input Features, G: Output Features

## Slide 21: Execution example of PP dataflow
Here, step refers to the duration in which producer writes a part of the intermediate matrix and consumer reads a part of the intermediate matrix
WR
Occupancy of the intermediate matrix inside the buffer =
RD
Accelerator
Matrix multiplications
Inside the global buffer
V: Vertices; N: Neighbors; F: Input Features, G: Output Features

## Slide 22: Data movement in Inter-phase Dataflows
Inter-phase dataflows describe the data reuse strategies between the two phases.
SEQ dataflow writes the complete intermediate matrix to the memory in Aggregation and then reads it in the Combination phase.
SP and PP dataflows reuse the data between the two phases, thus avoiding writing the entire intermediate matrix to the DRAM and reading it.
SP and PP dataflow reduce the data movement of the intermediate matrix by consuming right after producing

## Slide 23: Interdependence between dataflows
PP
SP
Here, the production and consumption of data are in the row-major order. Therefore, the outermost loop is V in both the cases and inner loops can be re-ordered.
AGG
for v=1:V
for f=1:F
for n=1:N
CMB
for v=1:V
for g=1:G
for f=1:F
For more details on dependencies between the loop orders and the tile sizes, and for other ways to stage the computations please refer to the pre-print of the paper https://arxiv.org/pdf/2103.07977.pdf
SP and PP dataflows are interdependent.

## Slide 24: GNN Dataflow Taxonomy
<Inter Phase><Phase order>(<Intra Phase Agg>, <Intra Phase Cmb>)
Inter-Phase dataflows - Seq, SP, PP
Phase Order - AC, CA
Intra-Phase dataflow (Examples - VsGsFt for Combination).
V: Vertices; N: Neighbors; F: Input Features, G: Output Features
Notes: So now that we have looked at the inter-phase and intra-phase dataflows, the compete dataflow description is as follows:

## Slide 25: GNN dataflow DSE
Our taxonomy can capture the dataflows used by the state-of-the-art GNN accelerators. For more details, please refer to the paper.

## Slide 26: Qualitative observations in Inter-phase dataflows
SEQ – Any intra-phase dataflow ; SP and PP constrained.
Within SP, for intermediate matrix to stay in the register file, T_V should be equal for both phases and so does T_F. T_N=1. So, higher data movement reduction puts more constraints on the dataflow choices. We call this SP-Optimized and we refer to other SP datafloes as SP-Generic.
PP requires balancing Aggregation and Combination.
These dataflows have numerous tradeoffs, thus detailed quantitative modeling of these phases is required.

## Slide 27: OMEGA Cost Model
To this end, OMEGA encodes the analytical model of the inter-phase dataflows
OMEGA builds upon STONNE (Munoz-Martinez et al., IISWC 2021), which accurately models the hardware for MAERI which is a flexible accelerator.
We also add support for indexing logic and memory controllers for SpMM which is in addition to MAERI (CONV/GEMM) and SIGMA(SpGEMM) and we use the MAERI accelerator for DenseGEMMs.
Dimensions
OMEGA
STATS
STONNE SpMM parameter translation
STONNE GEMM parameter translation
Graph (CSR)
STONNE()
SpMM Accelerator
GEMM Accelerator (MAERI)
①
②
SpMM
-Timestamps
-Runtime
-Buffering
GEMM
-Timestamps
-Runtime
-Buffering
INTER-PHASE COST MODEL
③
Runtime
Energy
Buffer
INPUT
Dataflows+Tile sizes
Hardware Parameters

## Slide 28: Some key Analytical Equations
For more detailed explanation, please refer to the pre-print of the paper section 4
Inter-phase Dataflows | Intermediate buffer storage required | Runtime | Global Buffer Accesses
Seq |  |  | 
SP-Generic-rows |  |  | 
SP-Optimized |  |  | 
PP-rows |  |  | 
Inter-phase Dataflows | Intermediate buffer storage required | Runtime | Global Buffer Accesses
Seq |  |  | 
SP-Generic-rows |  |  | 
SP-Optimized |  |  | 
PP-rows |  |  | 

## Slide 29: Opening up OMEGA on docker
cd /OMEGA/omega-code

## Slide 30: Building OMEGA
make omega

## Slide 31: Using git
git clone https://github.com/stonne-simulator/omega.git

## Slide 32: Inputs: OMEGA command line interface
vim example_simulation.sh
Dimensions
  -V, -F, -G, -E (Edges, required for parsing)
Tile sizes for both phases
  -T_Va, -T_N, -T_Fa, -T_Vc, -T_G, -T_Fc
Hardware Parameters
  -Pe_agg, -Pe_cmb, -dn_bw_agg, -dn_bw_cmb, -rn_bw_agg, -rn_bw,cmb
Path to Input files for the adjacency matrix (CSR representation)
  -vertex_path, edge_path
./omega -V=1168 -F=28 -G=2 -E=2590 -T_Va=18 -T_N=1 -T_Fa=28 -T_Vc=18 -T_G=1 -T_Fc=28 -pe_agg=512 -pe_cmb=512 -dn_bw_agg=512 -rn_bw_agg=512 -dn_bw_cmb=512 -rn_bw_cmb=512 -vertex_path="sample_graphs/vertex_mutag_batch64.txt" -edge_path="sample_graphs/edge_mutag_batch64.txt" cd sample_graphs vim edge_mutag_batch64.txt
vim vertex_mutag_batch64.txt

## Slide 33: Parameter translation to STONNE
VAGG, GNN→ MSpMM
FAGG, GNN→ NSpMM
NGNN→ K_non-zeroSpMM
VCMB, GNN→ MGEMM
FCMB, GNN→ KGEMM
GGNN→ NGEMM

## Slide 34: OMEGA wrapper
vim stonne/src/omega.cpp
The OMEGA wrapper is omega.cpp and consists of the following parts-
  Parsing the command line parameters
  Reading the matrices
  Instantiating and running STONNE for SpMM
  Repeating 2. and 3. for GEMM.
  Inter-phase analytical equations. Please note that currently there are additional equations to enable T_VAGG=1.

## Slide 35: Running example simulation
source example_simulation.sh

## Slide 36: Output: Printed Results
SpMM RF statistics
SpMM Global Buffer (GB) statistics
GEMM RF statistics
GEMM Global Buffer Accesses
Aggregation and Combination runtimes
PP cycles (nPEs=AGG+CMB)
SP cycles (These make sense only if PE_agg=PEcmb and then nPEs=PE_AGG)
Intermediate GB occupancies
GB accesses

## Slide 37: Intra-phase stats

## Slide 38: Inter-phase stats

## Slide 39: Changing the tile sizes
cp example_simulation.sh example2_simulation.sh
vim example2_simulation.sh
./omega -V=1168 -F=28 -G=2 -E=2590 -T_Va=170 -T_N=1 -T_Fa=3 -T_Vc=170 -T_G=1 -T_Fc=3 -pe_agg=512 -pe_cmb=512 -dn_bw_agg=512 -rn_bw_agg=512 -dn_bw_cmb=512 -rn_bw_cmb=512 -vertex_path="sample_graphs/vertex_mutag_batch64.txt" -edge_path="sample_graphs/edge_mutag_batch64.txt"
source example2_simulation.sh
We observe that performance improves with these tile sizes

## Slide 40: Changing the bandwidth
cp example_simulation.sh example3_simulation.sh
vim example3_simulation.sh
./omega -V=1168 -F=28 -G=2 -E=2590 -T_Va=18 -T_N=1 -T_Fa=28 -T_Vc=18 -T_G=1 -T_Fc=28 -pe_agg=512 -pe_cmb=512 -dn_bw_agg=128 -rn_bw_agg=128 -dn_bw_cmb=128 -rn_bw_cmb=128 -vertex_path="sample_graphs/vertex_mutag_batch64.txt" -edge_path="sample_graphs/edge_mutag_batch64.txt"
source example3_simulation.sh
As expected, performance deteriorates with decrease in BW
For details on other experiments, please look at the preprint section 5

## Slide 41: Summary
Several important workloads across ML and HPC have multiphase matrix computations and the dataflows that can exploit reuse between the phases are crucial.
We capture the design-space of these dataflows using a succinct taxonomy. We contrast these dataflow choices and highlight the trade-offs in these dataflows.
We propose an analytical framework for cost-modelling dataflows.

## Slide 42: Acknowledgements
Co-Design Center for Artificial Intelligence-Focused Architectures and Algorithms Funded By